## Slide 1: Optimisation of LEO satellites Doppler shift compensation by reducing TLE errors and improving trajectory prediction algorithms
Kushagra Shrivastava1 & Rajvrat Thapliyal1
Supervisor: A/Prof Abhishek Rai2
Lab Mentors: Ma Yuling2, Yuan Fangxing2, Fu Naifeng3
SPS Mentors: Lim Yi Zhen1, Hillson Hung1
1 Special Program in Science (SPS), National University of Singapore, Singapore
2 Satellite Technology and Research (STAR) Centre, National University of Singapore, Singapore
3 School of Marine Science and Technology, Tianjin University, China
SP3172 Final Presentation
*Stock 3D models

## Slide 2: Overview
Section 1
Why did we do this research?

## Slide 3: Why is Low-Earth Orbit (LEO) important?
Overview
If you want to…
Image Sources: https://www.swyvl.io/blog/the-role-of-satellite-imagery-in-disaster-management , https://www.youtube.com/watch?v=3gmogp5-xXA,
Disaster Management
Telecommunication
Internet
Low-Earth Orbit Satellites
Orbits at least 6 times a day
Low Altitude (~500 km)
VERY high speed (~10 km/s)
(Hoots et al. 1998)

## Slide 4: The issue with LEO
Overview
“With great speed comes great problems”
Doppler Shift: Movement changes the communication frequency!
Satellite
Ground Station
If we cannot predict the doppler shift, we cannot communicate with the satellite!
Position and velocity prediction
Our research
(Yll, 2018)

## Slide 5: Current methods for prediction: TLE
STARLINK-11548
1 62829U 25019A 25054.47292006 .00001794 00000+0 13172-4 0 9998
2 62829 42.9999 73.2396 0001638 288.8584 71.2109 15.77857668 4220
Inclination
Epoch Year & Julian Day Fraction
Right Ascension of the Ascending Node
Eccentricity
Argument of Perigee
Drag
Mean Anomaly
Mean motion
Two-Line Element
All the parameters to be used for predicting the orbit, with a time at which the TLE was made.
Overview
(Celestrak.org, 2025; NORAD, 2025)

## Slide 6: Current Method for prediction: SGP4
Simplified General Perturbation Model 4 accounts for drag, solar radiation, Earth’s non-spherical shape, and the moon.
Input parameters
One TLE
One date at which we want to make a prediction, t
Position at t
Velocity at t
Magical Calculations
SGP4
Output parameters
Overview
TLE has inherent errors and SGP4 accumulates error!
Our research explores two independent algorithms that can reduce this error.
So what’s the issue?
(Hoots et al., 1988)

## Slide 7: MCS Algorithm
Section 2
Our implementation and the results

## Slide 8: What is the goal here?
Reduce the inherent errors in TLE
MCS Algorithm
A lot of TLEs
1 Optimised TLE
Reference TLE
(Liu et al., 2023)
2 variables: Number of TLEs and the reference TLE

## Slide 9: Methodology Step 1: Loss Function
Take N TLEs
TLE #1
TLE#2
TLE#3
TLE#N
…
t1
t2
t3
t4
Each TLE has a time associated with it
MCS Algorithm
(Liu et al., 2023)

## Slide 10: Methodology Step 1: Loss Function
TLE #1
TLE#2
TLE#3
TLE#N
…
t1
t2
t3
tN
Each TLE has a time associated with it
xt1, vt1
xt2, vt2
xt3, vt3
xtN, vtN
Take N TLEs
…
Using SGP4, calculate the position, x, and velocity, v, at that time
MCS Algorithm
(Liu et al., 2023)

## Slide 11: Methodology Step 1: Loss Function
TLE #1
TLE#2
TLE#3
TLE#N
…
t1
t2
t3
tN
Each TLE has a time associated with it
xt1, vt1
xt2, vt2
xt3, vt3
xtN, vtN
Take N TLEs
…
Using SGP4, calculate the position, x, and velocity, v, at that time
TLE#3
t2
t3
tN
t1
…
Choose a reference TLE, and calculate x and v at all times using SGP4
xt1r, vt1r
xt2r, vt2r
xt3r, vt3r
xtNr, vtNr
…
MCS Algorithm
(Liu et al., 2023)

## Slide 12: Methodology Step 1: Loss Function
xt1, vt1
xt2, vt2
xt3, vt3
xtN, vtN
…
Subtract the two values together and square them
TLE#3
xt1r, vt1r
xt2r, vt2r
xt3r, vt3r
xtNr, vtNr
…
Respective TLEs
-
-
-
-
(Δx1)2, (Δv1)2
(Δx2)2, (Δv2)2
(Δx3)2, (Δv3)2
(Δx4)2, (Δv4)2
…
=
=
=
=
MCS Algorithm
(Liu et al., 2023)

## Slide 13: Methodology Step 1: Loss Function
Create the loss function
(Δx1)2, (Δv1)2
(Δx2)2, (Δv2)2
(Δx3)2, (Δv3)2
(Δx4)2, (Δv4)2
…
Sum everything together, Lstandard
Only sum position difference, Lpos
Only sum velocity difference, Lvel
Weighted sum, Lweighted
(Multiply all positions by 10-3)
Performed the best
Ideal case scenario
Lstandard = 0
But that is near impossible, and thus we instead try to minimize it
MCS Algorithm
Change the reference TLE such that we can minimize Lstandard

## Slide 14: Methodology 2: Monte-Carlo Simplex
MCS Algorithm
Algorithm to find the global minimum value of Lstandard
Lstandard
Parameters
Local Minima
Global Minima

## Slide 15: Methodology 2: Monte-Carlo Simplex
MCS Algorithm
(Liu et al., 2023)
Take the reference TLE
Create vertices of simplex
(1 original and 7 perturbed)
Simplex transforms
Finds minima
Nelder-Mead Simplex
Animation created using Manim
(a, b)
(a, b+1)
(a+1, b)
Lstandard

## Slide 16: Methodology 2: Monte-Carlo Simplex
MCS Algorithm
(Liu et al., 2023)
Take the reference TLE
Create vertices of simplex
(1 original and 7 perturbed)
Simplex transforms
Finds minima
Monte-Carlo Simplex
Animation created using Manim
Repeat this 5000 times, changing the reference TLE a little bit for each run.
Lstandard

## Slide 17: Methodology 2: Monte-Carlo Simplex
MCS Algorithm
Distribution of optimal values for 1 parameter
Mean of normal distribution is the final optimised value
(Liu et al., 2023)

## Slide 18: Results 1: Change reference TLE
MCS ALWAYS performs WORSE than simple SGP4.
X-axis is number of days AFTER the last TLE in the set.

## Slide 19: Results 2: Change number of TLEs
MCS ALWAYS performs WORSE than simple SGP4.
X-axis is number of days AFTER the last TLE in the set.

## Slide 20: Why did it perform so bad?
Hypothesis 1: Physics uninformed
Hypothesis 2: TLE dataset issue
Time
Time when satellite was closest to Earth
Mean Anomaly: Speed of satellite if it had a circular orbit
Mean Motion: Number of revolutions in a day
MCS randomly changes parameters value without following any physical laws
Orbit of a satellite
TLE #1
TLE #2
TLE #3
TLE #4
TLE #5

## Slide 21: ML-SGP4 Model
Section 3
Our implementation and the results
Notes: Thank you kush, I will now introduce the ML-dSGP4 Model and our experiments with it

## Slide 22
SGP4
ML-SGP4
The original algorithm
SGP4 integrated into an ML model
Neural Networks
A common Machine Learning (ML) model
What is ML-SGP4?
Notes: So what is ML-dsgp4?
To understand this Model lets break it down into some simpler parts
Originally we had the SGP4 algorithm. Acciarini et al then created a differentiable version of SGP4 called dsgp4
This allows the dsgp4 to be implemented within Machine learning frameworks.
Acciarini et al then created ML-dsgp4, a machine learning model which integrates Dsgp4 Into its architectures, making it physics-aware **explain something about physics awareness**
ML-dsgp4 be the focus of our study.

## Slide 23: ML-SGP4 Architecture
2
Neural Network 1
1
Raw TLEs
3
2
1
Optimised TLEs
Input
Output
Correction Factors
…
Correction Factors
…
Applied to TLE elements
TLE Correction Module
1
Unoptimized State vectors (Si)
SGP4
Neural Network 2
Optimised State Vectors
Input
Output
Correction Factors
…
Correction Factors
…
Applied to Si’s elements
2
1
dSGP4 Correction Module
(Acciarini et al., 2025)
Notes: Now I’d like to walk you through the ML-dSGP4 architecture.
First we obtain our Raw unoptimized TLEs.
We feed the TLEs into the first neural network in ML-dSGP4.
The neural network will learn the errors in TLE and output the correction factors that will multiplicatively be multiplied with the original TLE elements to finally output the final optimised TLE.
Now you might have gotten lost through this explanation but for the purpose of this presentation you can simply replace all these components in the middle and interpret as a black box, where suboptimal tles are inputted and outputs optimal tles.

## Slide 24: ML-SGP4 Architecture
2
Neural Network 1
1
Raw TLEs
3
2
1
Optimised TLEs
Input
Output
Correction Factors
…
Correction Factors
…
Applied to TLE elements
TLE Correction Module
1
Unoptimized State vectors (Si)
SGP4
Neural Network 2
Optimised State Vectors
Input
Output
Correction Factors
…
Correction Factors
…
Applied to Si’s elements
2
1
dSGP4 Correction Module
(Acciarini et al., 2025)
Notes: Now I’d like to walk you through the ML-dSGP4 architecture.
First we obtain our Raw unoptimized TLEs.
We feed the TLEs into the first neural network in ML-dSGP4.
The neural network will learn the errors in TLE and output the correction factors that will multiplicatively be multiplied with the original TLE elements to finally output the final optimised TLE.
Now you might have gotten lost through this explanation but for the purpose of this presentation you can simply replace all these components in the middle and interpret as a black box, where suboptimal tles are inputted and outputs optimal tles.

## Slide 25: ML-SGP4 Architecture
2
Neural Network 1
1
Raw TLEs
3
2
1
Optimised TLEs
Input
Output
Correction Factors
…
Correction Factors
…
Applied to TLE elements
TLE Correction Module
1
Unoptimized State vectors (Si)
SGP4
Neural Network 2
Optimised State Vectors
Input
Output
Correction Factors
…
Correction Factors
…
Applied to Si’s elements
2
1
Correction Module
(Acciarini et al., 2025)
Notes: Now I’d like to walk you through the ML-dSGP4 architecture.
First we obtain our Raw unoptimized TLEs.
We feed the TLEs into the first neural network in ML-dSGP4.
The neural network will learn the errors in TLE and output the correction factors that will multiplicatively be multiplied with the original TLE elements to finally output the final optimised TLE.
Now you might have gotten lost through this explanation but for the purpose of this presentation you can simply replace all these components in the middle and interpret as a black box, where suboptimal tles are inputted and outputs optimal tles.

## Slide 26: ML-SGP4 Architecture Overview
Optimised State Vectors
2
1
2
1
Raw TLEs
TLE correction module
SGP4
correction module
Learns and corrects TLE error
Learns and corrects SGP4 propagation error
(Acciarini et al., 2025)
Notes: Now I’d like to walk you through the ML-dSGP4 architecture.
First we obtain our Raw unoptimized TLEs.
We feed the TLEs into the first neural network in ML-dSGP4.
The neural network will learn the errors in TLE and output the correction factors that will multiplicatively be multiplied with the original TLE elements to finally output the final optimised TLE.
Now you might have gotten lost through this explanation but for the purpose of this presentation you can simply replace all these components in the middle and interpret as a black box, where suboptimal tles are inputted and outputs optimal tles.

## Slide 27: Training ML- SGP4 from Scratch: Set-up and Challenges

## Slide 28: Preliminary Model: A larger Dataset
Properties | Original ML-SGP4 dataset | Updated ML-SGP4 dataset
Satellite Count | ~1500 | ~6000
Datapoints / Rows | ~9 Million | ~288 Million
Year Created | 2023 | 2025
Properties |  | 
Satellite Count | ~1500 | ~6000
Datapoints / Rows | ~9 Million | ~288 Million
Year Created | 2023 | 2025
Generally…
Larger dataset = More accurate Model
(Acciarini et al., 2025)
Notes: Initially our goal was to make a better version of ML-Dsgp4 by using the same model template and training it on a larger updated version of the satellite dataset acciarani et al used to train their model on.
The original dataset only consisted of SPACEX’s Starlink satellites as they are considered LEO satellites and their data is opensource.
However in the year 2023, when the paper was published, acciarani et al’s dataset only included 1500 satellites, corresponding to about 9million rows of data in their original dataset.
Today there are over 6000 starlink satellites and we attempted to leverage the use of more satellites in the dataset to train a more accurace version of ml-dsgp4 as generally, ML models trained on more data will give better performance as the models can more accurately tune themselves with more data and make more accurate prediction.
We made use of NSCC’s supercomputer to train our model. However the projected training time was determined to be over 70 days, which made training the large model infeasible

## Slide 29: Preliminary Model: Infeasible Training Time
Preliminary Model:
~288 Million Datapoints
12 hours of training on NSCC’s supercomputer
0.70% of training completed
Extrapolated Training Time:
~70 Days
Notes: We made use of NSCC’s supercomputer to train our model. However the projected training time was determined to be over 70 days, which made training the large model infeasible

## Slide 30: Preliminary Model: Inefficient Source Code
Index | Period | TLEs
1 | P | TLE1
2 | P | TLE2
3 | P3 | TLE3
… | … | …
207,178,987 | P207,178,987 | TLE207,178,987
Index | Period | TLEs
1 |  | TLE1
2 |  | TLE2
3 | P3 | TLE3
… | … | …
207,178,987 | P207,178,987 | TLE207,178,987
Training Dataset
Python TLE Objects
TLE Object1
TLE Object2
TLE Object3
…
TLE Object207,178,987
Slow, iterative parsing of the training dataset
TLE Objects Data frame
Notes: We made use of NSCC’s supercomputer to train our model. However the projected training time was determined to be over 70 days, which made training the large model infeasible

## Slide 31: ML- SGP4: The suboptimal training scheme
Original ML-SGP4 :
Trains on a dataset with many satellites
Not all satellites have the same error propagation pattern
But…
Figure 2: Position error propagation over time for various satellites.

## Slide 32: ML- SGP4: The suboptimal training scheme
Trains on a dataset with many satellites
Not all satellites have the same error propagation pattern
But…
Model’s Aggregated Fit
Figure 2: Position error propagation over time for various satellites.
Original ML-SGP4 :

## Slide 33: ML- SGP4: The suboptimal training scheme
Model’s Aggregated Fit
Trains on a dataset with many satellites
Not all satellites have the same error propagation pattern
But…
Consistent Error reflected in Model
Causing
Errors
Figure 2: Position error propagation over time for various satellites.
Original ML-SGP4 :

## Slide 34: Mini-ML- SGP4: Overcoming Drawbacks
Suboptimal training method
Original ML-SGP4’s Flaws
Limits model’s predictive accuracy
Train each Mini Model on a dataset for one satellite
Impact on Performance
Our Solution
Mini-ML-SGP4
Inefficient Source Code
Slow training time
Use smaller datasets
(Acciarini et al., 2025)
Notes: Therefore to overcome the long training time and to boost the accuracy of the model we propose Mini-ML-dSGP4
Mini Ml-dsgp4 makes use of the same ML-Dsgp4 architecture but trained on a dataset for only a single satellite. This allows the model to make Accurate predictions for its specific satellite while leveraging a far smaller dataset to reduce training time.
To evaluate the model’s performance across different satellites we use satellites with the highest orbital period, intermediate orbital period and lowest orbital period in the datasets.

## Slide 35: Data Preparation
Full Dataset | 
Rows | 288,305,762
Minimum
Period Satellite
STARLINK 6060 Mini Dataset | 
Rows | 77,779
STARLINK 5350 Mini Dataset | 
Rows | 43,210
STARLINK 2561 Mini Dataset | 
Rows | 25,926
Intermediate Period Satellite
Maximum
Period Satellite
STARLINK 2561 Mini Model
STARLINK 5350 Mini Model
STARLINK 6060 Mini Model
Satellite Selection Criteria
Datasets
Final Mini Models

## Slide 36: Evaluation set up
(More negative better)
STARLINK XXXX’s Mini Model
Original
ML-SGP4
SGP4
Prediction – True Ground
Prediction – True Ground
Prediction – True Ground
ML-SGP4 Loss
Mini Loss
SGP4 Loss
We finally get 2 success metric readings for each Mini Model
Notes: We can now evaluate our models
We compare our models against the original SGP4 propagator and the pretrained ML-dsgp4 propagator by acciarani et al.
We compute the difference between the error of the mini model and the rival models and plot a histogram of the frequency of the observered error differences.

## Slide 37: Results
Mini-ML- SGP4 consistently and significantly outperforms SGP4 and ML- SGP4 in reducing trajectory errors for low-period satellites.
Mini-ML-SGP4 overall underperforms with the highest period satellite
Starlink - 2561 Mini Model
Starlink - 5350 Mini Model
Starlink - 6060 Mini Model
Notes: Here are our results.
On X axis we have the magnitude of the error difference observed. And on the y axis we have the count of that error difference observed.
For starlink 2561 and Starlink XXX, we observe that the area under the graph in the negative region is far larger than each of their graphs in the positive region. _> This indicates that their mini models perform consistently better than their rival models.
Moreover we observe that the mean magnitude of their errors are well into the negative values, indicating that the error reduction by our models on average is substantially larger than the error reduced by the rival models.
However we do observe that the satellite with the highest performs the worst. As seen by a relatively even spread of the distribution about the 0 value, indicating that the mini model can do equally good or bad in comparison with SGP4 .**************improve**************
Although we can get a rough gauge that our models tend to deprove in performance as satellite period increases, further studies will need to be done to create more mini models for each satellite and evaluate their performance to deterministically derive a pattern in the model’s performance across satellite periods.

## Slide 38: Future Work and Conclusion
Section 4
So what next?

## Slide 39: Final words
MCS might be trash
Mini ML-∂SGP4 has good potential
How can we make them better?
Breaking down MCS and ML-∂SGP4 into their smaller components to identify sources of error
Tune ML-∂SGP4’s original architecture to improve its performance and make it physics informed.

## Slide 40: Acknowledgements
We would like to express our gratitude to STAR’s director, A/Prof Abhishek Rai, and Lab Mentors, Ma Yuling, Yuan Fangxing, and Dr Fu Naifeng for their constant support, feedback and patience throughout our journey. We also thank our SPS Mentors, Lim Yi Zhen and Hillson Hung, for constant and even last-minute feedback on the reports and presentations, and our SPS friends for the impromptu help in their specialized fields. Lastly, we would like to thank the National Supercomputing Centre (NSCC) Singapore for allowing us to use their resources.

## Slide 41: References
Acciarini, G., Baydin, A. G., & Izzo, D. (2025). Closing the gap between sgp4 and high-precision propagation via differentiable programming. Acta Astronautica, 226, 694–701. https://doi.org/https://doi.org/10.1016/j.actaastro.2024.10.063
Ali, I., Al-Dhahir, N., & Hershey, J. E. (1998). Doppler characterization for leo satellites. IEEE Trans. Commun., 46, 309–313. https://api.semanticscholar.org/CorpusID:206409378
Asraf, A., Surayuda, R. H., Ribah, A. Z., Kamirul, & Mukhayadi, M. (2021). Determination of mean orbital elements using gps data for lapan satellite daily operation. 2021 IEEE International Conference on Aerospace Electronics and Remote Sensing Technology (ICARES), 1–6. https://doi.org/10.1109/ICARES53960.2021.9665177
Barinov, R., Gai, V., Kuznetsov, G., & Golubenko, V. (2023). Automatic evaluation of neural network training results. Computers, 12, 26. https://doi.org/10.3390/computers12020026
Einstein, A. (1905). Zur elektrodynamik bewegter korper. Annalen der Physik, 322(10), 891–921. https://doi.org/10.1002/andp.19053221004
European Space Agency, Space Debris Office. (2024). ESA’s Annual Space Environment Report (tech. rep. No. ESA/GEN-DB-LOG-00288-OPS-SD) (Accessed: 2025-03-27). European Space Agency. Darmstadt, Germany. https://www.sdo.esoc.esa.int/environment_report/Space_Environment_Report_latest.pdf
Hoots, F. R., & Roehrich, R. L. (1988). Models for propagation of norad element sets (tech. rep. No. Spacetrack Report No. 3). CelesTrak. https://celestrak.org/NORAD/documentation/spacetrk.pdf
Hussain, W., Merig´o, J. M., Gil-Lafuente, J., & Gao, H. (2023). Complex nonlinear neural network prediction with iowa layer. Soft Computing, 27, 4853–4863. https://doi.org/10.1007/s00500-023-07899-2
Jason, Z., Zhang, K., & Grenfell, R. (2004). On the relativistic doppler effects and high accuracy velocity determination using gps.
Kelso, T. S. (2022). Norad two-line element set format [Accessed: 30 March 2025]. https://celestrak.org/NORAD/documentation/tle-fmt.php
Leakyrelu — pytorch 1.11.0 documentation. (n.d.). pytorch.org. https://pytorch.org/docs/stable/generated/torch.nn.LeakyReLU.html
Liu, J., Long, W., Wu, Y., Xu, J., Sang, J., & Lei, X. (2023). TLE orbit determination using simplex method. Geodesy and Geodynamics, 14(5), 438–455. https://doi.org/10.1016/j.geog.2023.03.004
National University of Singapore. (2024a). Galassia-2 satellite built by nus students successfully launched [Accessed: 2025-03-31]. https://news.nus.edu.sg/galassia-2-satellite-built-by-nus-students-successfully-launched/
National University of Singapore. (2024b). Successful launch of lumelite-4 to enhance maritime communications [Accessed: 2025-03-31]. https://news.nus.edu.sg/successful-launch-of-lumelite-4-to-enhancemaritime-communications/
NVIDIA. (n.d.). What is pytorch? NVIDIA Data Science Glossary. https://www.nvidia.com/en-us/glossary/pytorch/
Olson, M., Wyner, A., & Berk, R. (2018). Modern neural networks generalize on small data sets. In S. Bengio, H. Wallach, H. Larochelle, K. Grauman,
N. Cesa-Bianchi, & R. Garnett (Eds.), Advances in neural information processing systems (Vol. 31). Curran Associates, Inc. https://proceedings.neurips.cc/paper_files/paper/2018/file/fface8385abbf94b4593a0ed53a0c70f-Paper.pdf
Rojas, R. (1996). The backpropagation algorithm. Neural Networks, 149–182. https://doi.org/10.1007/978-3-642-61068-4_7
Space-track.org. (n.d.). www.space-track.org. https://www.space-track.org/auth/login
Tanh — pytorch 1.13 documentation. (n.d.). pytorch.org. https://pytorch.org/docs/stable/generated/torch.nn.Tanh.html
Yll, D. N. (2018). Doppler shift compensation strategies for leo satellite communication systems [Ph.D. Dissertation]. Universitat Politecnica de Catalunya. https://upcommons.upc.edu/bitstream/handle/2117/123510/DanielNietoYll_Doppler_compensation_for_LEO.pdf

## Slide 42: Thank you!
The template of this presentation was custom made in Microsoft PowerPoint 365
SP3172 Final Presentation
*Satellite is a free-to-use 3D stock model

## Slide 43: Additional Slides
Section 5

## Slide 44: How do we define our errors?
We work with past year’s data.
Important Note
t1
t0
t2
t3
tN
…
Actual position/velocity
Position/Velocity
Predicted position/velocity
Error = |Prediction – Actual|

## Slide 45: All TLE parameters
STARLINK-11548
1 62829U 25019A 25054.47292006 .00001794 00000+0 13172-4 0 9998
2 62829 42.9999 73.2396 0001638 288.8584 71.2109 15.77857668 4220
Satellite name
Satellite Number
International Designator
Inclination
Epoch Year & Julian Day Fraction
Right Ascension of the Ascending Node
1st derivative of mean motion
Eccentricity
2nd derivative of mean motion
Argument of Perigee
Drag
Mean Anomaly
Mean motion
Revolution number at epoch & checksum
Element Number & checksum
Ephemeris Type
Two-Line Element
Overview
(Celestrak.org, 2025; NORAD, 2025)

## Slide 51
Full Dataset |  | 
Split | Attribute Details | 
Train | Rows | 207,178,987
 | Period Range (min) | 89.32 – 95.60
Validation | Rows | 40,189,621
 | Period Range (min) | 95.62 -96.23
Test | Rows | 40,937,154
 | Period Range (min) | 95.68 – 86.23
Medium Dataset |  | 
Split | Attribute Details | 
Train | Rows | 20742
 | Period Range (min) | 89.32 - 95.60
Validation | Rows | 4024
 | Period Range (min) | 95.62 - 96.23
Test | Rows | 4099
 | Period Range (min) | 95.68 – 96.23
“STARLINK 6060” - Mini Dataset | 
Split | Rows
Train | 50556
Validation | 13654
Test | 13569
Randomly sample 1% of each spit
Filter for the satellite with maximum period
Randomly select a satellite with a period between minimum and maximum
Filter for the satellite with minimum period
“STARLINK 5350” - Mini Dataset | 
Split | Rows
Train | 28086
Validation | 7539
Test | 7585
“STARLINK 2561” - Mini Dataset | 
Split | Rows
Train | 16852
Validation | 4477
Test | 4597

## Slide 52
 | SGP4 vs Mini Model |  | ML-dSGP4 vs Mini Model | 
Satellite | Mini Model Better | Mini Model Worse | Mini Model Better | Mini Model Worse
STARLINK - 2561 | 4200.88 | 842.65 | 4810.56 | 1122.51
STARLINK - 5350 | 34.32 | N/A | 16.86 | 8.26
STARLINK 6060 | 3803.40 | 218.39 | 4495.74 | 867.87